## Slide 1: Data Compression for comet interceptor

## Slide 2: Project Overview
Magnetometer data will be provided as 14 bit signed integers
Create algorithms to achieve the highest possible compression ratio
Compression technique must be lossless
Optimise highest compression ratio versus lowest latency
Account for low processing capability due to hardware limitations

## Slide 3: Difference encoding
Initial Value Difference
Previous Value Difference
1200
1205
1210
1190
1203
1200-1200
1205-1200
1210-1200
1190-1200
1203-1200
0
5
10
-10
3
1200
1205
1210
1190
1203
1200-1200
1205-1200
1210-1205
1190-1210
1203-1190
0
5
5
-20
13

## Slide 4: Difference ENCoding

## Slide 5: Huffman encoding

## Slide 6: Golomb encoding
Optimal M value inconsistent across axes
Provides compression ratio of 31%
14
q=2
r=4
If r<3
110
b=3
Else
2 bits
3 bits for 4+3 (111)
110111
M=5
N
q=floor(N/M)
r=N-qM
If r<2b-M
Unary code
b=ceil(log2M)
Else
b-1 bits for r
b bits for r+2b-M
Full Binary Form

## Slide 7: Review and further work
Golomb coding with difference recursion provides the best compression ratio of 31%
Is there a perfect sample size for lowest latency and best compression ratio?
Can we dynamically allocate an M value for Golomb coding?
How can we change sample size dynamically to account for periods of inactivity?

## Slide 8: Thank you for your attention
Any Questions?

## Slide 9
N (M=3) | Floor Value | Unary | Remainder | Binary | Combined
0 | 0 | 0 | 0 | 0 | 00
1 | 0 | 0 | 1 | 01 | 001
2 | 0 | 0 | 2 | 10 | 010
3 | 1 | 10 | 0 | 0 | 100
4 | 1 | 10 | 1 | 01 | 1001
5 | 1 | 10 | 2 | 10 | 1010
6 | 2 | 110 | 0 | 0 | 1100
7 | 2 | 110 | 1 | 01 | 11001
8 | 2 | 110 | 2 | 10 | 11010
9 | 3 | 1110 | 0 | 0 | 11100
10 | 3 | 1110 | 1 | 01 | 111001
14
q=2
r=4
If r<3
110
b=3
Else
2 bits
3 bits for 4+3 (111)
110111
M=5
N
q=floor(N/M)
r=N-qM
If r<2b-M
Unary code
b=ceil(log2M)
Else
b-1 bits for r
b bits for r+2b-M
Full Binary Form
1200
1205
1210
1190
1203
1200-1200
1205-1200
1210-1200
1190-1200
1203-1200
0
5
10
-10
3
1200
1205
1210
1190
1203
1200-1200
1205-1200
1210-1205
1190-1210
1203-1190
0
5
5
-20
13